## Slide 1
COMP90018 Mobile Computing Systems Programming
WEEK 4 – Sensors
Weiwei Jiang
weiwei.jiang@student.unimelb.edu.au

## Slide 2
CONTENTS
1
Sensor
2
Compass
3
Barometer
4
Location

## Slide 3
Sensor

## Slide 4: Sensor
Most Android-powered devices have built-in sensors that measure motion, orientation, and various environmental conditions.
https://developer.android.com/guide/topics/sensors/sensors_overview

## Slide 5: Sensor – Motion Sensors
Motion sensors
These sensors measure acceleration forces and rotational forces along three axes, include
Accelerometers
Gravity sensors
Gyroscopes
Rotational vector sensors
https://developer.android.com/guide/topics/sensors/sensors_motion.html

## Slide 6: Sensor – Environmental sensors
Environmental sensors
These sensors measure various environmental parameters, include
Ambient air temperature
Illuminance (light)
Ambient air pressure
Ambient humidity
Device temperature
https://developer.android.com/guide/topics/sensors/sensors_environment.html

## Slide 7: Sensor – Position sensors
Position sensors
These sensors measure the physical position of a device, include
Orientation sensors
Magnetometers
https://developer.android.com/guide/topics/sensors/sensors_position.html

## Slide 8
Barometer
- Read sensor

## Slide 9: Barometer
A barometer is a scientific instrument that is used to measure air pressure in a certain environment. Pressure tendency can forecast short term changes in the weather.

## Slide 10: Barometer Sensor
Barometers are used for monitoring the ambient air pressure in hPa (or mbar).
https://developer.android.com/reference/android/hardware/Sensor.html#TYPE_PRESSURE

## Slide 11: Barometer – permission
AndroidManifest.xml

## Slide 12: Barometer – get sensor data
Barometer.java

## Slide 13: Barometer – get sensor data
MainActivity.java

## Slide 14: SensorEventListener
Used for receiving notifications from the SensorManager when there is new sensor data.
https://developer.android.com/reference/android/hardware/SensorEventListener

## Slide 15: Barometer Demonstration

## Slide 16
Compass
- A complete sensor-based app

## Slide 17: Accelerometer
Measures the acceleration force in m/s2 that is applied to a device on all three physical axes (x, y, and z), including the force of gravity.
https://developer.android.com/reference/android/hardware/Sensor.html#TYPE_ACCELEROMETER

## Slide 18: Magnetometer
Measures the ambient geomagnetic field for all three physical axes (x, y, z) in μT.
https://developer.android.com/reference/android/hardware/Sensor.html#TYPE_MAGNETIC_FIELD

## Slide 19: For Reading – Calculate Acceleration
Conceptually, an acceleration sensor determines the acceleration that is applied to a device (Ad) by measuring the forces that are applied to the sensor itself (Fs) using the following relationship:
However, the force of gravity is always influencing the measured acceleration according to the following relationship:

## Slide 20: For Reading – Low-Pass Filter
A low pass filter allows the low frequencies to pass while blocking the high frequencies.
http://philstech.blogspot.com/2012/04/quadcopter-accelerometer-data-filtering.html

## Slide 21: For Reading – Low-Pass/High-Pass Filter
To measure the real acceleration of the device can be achieved by applying a high-pass filter. Conversely, a low-pass filter can be used to isolate the force of gravity.
https://developer.android.com/guide/topics/sensors/sensors_motion#java

## Slide 22: For Reading – getRotationMatrix
Computes the inclination matrix I as well as the rotation matrix R transforming a vector from the device coordinate system to the world's coordinate system.
https://developer.android.com/reference/android/hardware/SensorManager.html#getRotationMatrix(float[],%20float[],%20float[],%20float[])

## Slide 23: For Reading – getRotationMatrix
R is the identity matrix when the device is aligned with the world's coordinate system, that is, when the device's X axis points toward East, the Y axis points to the North Pole and the device is facing the sky.

## Slide 24: For Reading – getOrientation
Computes the device's orientation based on the rotation matrix.
https://developer.android.com/reference/android/hardware/SensorManager.html#getOrientation(float%5B%5D,%2520float%5B%5D)

## Slide 25: Compass – Permission
AndroidManifest.xml

## Slide 26: Compass – Get sensor data
Compass.java

## Slide 27: Compass – Demonstration

## Slide 28
Location

## Slide 29: Location
One of the unique features of mobile applications is location awareness.
Mobile users bring their devices with them everywhere, and adding location awareness to your app offers users a more contextual experience.

## Slide 30: Location Demonstration – Native
Step 1:
You need a LocationManager
A Service does the low-level sensing : Context.LOCATION_SERVICE
Register a LocationListener

## Slide 31: Location Demonstration – Native
Step 2 (Permission Check For Location):
Location Sensing requires Permission from users;
API 23 or above needs runtime Permission Check.

## Slide 32: Location Demonstration – Native
Required Perimissions:
<uses-feature android:name="android.hardware.location.network" />
<uses-feature android:name="android.hardware.location.gps" />

## Slide 33: Location Demonstration – Native

## Slide 34: Location Demonstration – Google API
The ApiDemos repository on GitHub includes samples that demonstrate the use of location on a map.
https://github.com/googlemaps/android-samples/blob/master/ApiDemos

## Slide 35: Location Demonstration – Google API
Get your own API key for Google Map API:
https://developers.google.com/maps/documentation/android-sdk/get-api-key

## Slide 36: Location Demonstration – Google API